# Attachment J:  Resource Recovery

This attachment covers the combustion of waste for the purposes of energy generation or emissions control.

Description	EIC Code	CES Number

Resource recovery	099-080-0012-0000	83055

Municipal waste disposal	120-122-0242-0000	57281

## Landfill Gas Recovery

Methane and small amounts of VOCs are by-products of solid waste decomposition.  Landfills are the largest source of anthropogenic methane in the U.S. and contribute 35% of the total amount of methane produced by human sources (EPA, 2001a).  Landfill gas recovery systems reduce methane and VOC emissions at landfills and/or generate energy from the waste gases.  Energy-generating systems generally use landfill gas-fired turbines, while simple disposal systems employ flares.  Landfill gas (LFG) recovery is increasing nationwide, with the fastest growth in California (EPA, 2001a).

### Emission Factors

LFG recovery systems produce emissions of combustion by-products.  Table 1 lists emission factors that were selected for use.  Note that two chapters of EPA’s AP-42 guidance document offer emission factors for LFG turbines.  The factors from Chapter 3.1 (Stationary Gas Turbines) were selected for use in this analysis because the EPA assigned them higher quality ratings.

Table 1.   Emission factors for combustion of landfill gas (EPA, 2000; EPA, 1998).

| Process a | SO2 b | NOx | CO | TOCc | VOCd | Total PMe |
| --- | --- | --- | --- | --- | --- | --- |
| Landfill gas Fired Turbinesf | 18 | 56 | 176 | 765 | 5.2 | 0.92 |
| Flared Landfill gas | 7.9 | 4.0 | 75.0 | 126.6 | 1.69(10-9 | 1.7 |

a  Emission factors are expressed in units of lb pollutant/million standard cubic feet (106scf) of landfill gas combusted.

b The emission factor for SO2 is based on the EPA’s (1998) reported average sulfur content, 46.9 ppmv.

c  Landfill gases are comprised of more than 98% methane.  TOC emissions are assumed to be approximately equal to methane emissions.  The TOC emission factor was estimated by applying the reported methane control efficiency (EPA, 1998) to the total mass of methane recovered.  In order to convert methane volume to methane mass, the following conversion rate was applied:  42,198 lbs CH4/106scf CH4.

d The VOC emission factor was estimated by applying the EPA’s (1999; 1998) hydrocarbon speciation profile for LFG (VOC 1.2%, methane 98.7%, ethane 0.1% by weight) and the EPA’s reported flare combustion efficiency of 99.2% for NMOC.

e According to the EPA (1998) total PM emissions are equivalent to PM10 emissions.

f The emission factors for turbines are converted from the reported units of lb pollutant/MMBtu to lb pollutant/106scf by applying the EPA’s (2000) average landfill gas heating value, 400 Btu/scf.

### Activity Data

A list of facilities that combust landfill gases for energy generation is available from the U.S. Landfill Methane Outreach Program (EPA, 2001c).  According to LMOP, only four landfills in CCOS II counties (listed below) currently convert landfill gas to energy.  In addition, the Sacramento Air Quality Management District provided information that the Sacramento County Landfill (Kiefer) has landfill gas-to-energy capability.  The LMOP database provides estimates of potential methane generation.  However for consistency, we will use the estimates of landfill gas generation that were presented in Attachment B (Waste Disposal).  The estimates from Attachment B (listed below) agree within 25% of the LMOP estimates.

- Sacramento City Landfill produces 996 tons CH4/year (uncontrolled) or 47 MMscf/year.

- Union Mine Disposal Site (in El Dorado) produces 2,331 tons CH4/year (uncontrolled) or 111 MMscf/year.

- Yolo County Central Landfill produces 10,457 tons CH4/year (uncontrolled) or 496 MMscf/year.

- Sacramento County Landfill (Kiefer) produces 41,464 tons CH4/year (uncontrolled) or 1,966 MMscf/year.

Unfortunately, landfill-specific information regarding the installation of flares is unavailable.  However, the California Energy Commission (CEC) has prepared a draft greenhouse gas inventory for the State of California that includes an estimate of the statewide quantity of flared LFG:  6.3 million metric tons of CO2 equivalent (15,000 MMscf CH4).  At the time of this writing, the CEC inventory is in draft form and is noted “Do not cite or quote.”  However, because the inventory prepareres (ICF Consulting) had access to confidential survey information regarding sales and distribution of flares to landfills, this estimate is taken to be the most accurate currently available.  For future updates to the inventory, the technical contact for the CEC’s greenhouse gas inventory is Mr. Guido Franco of the California Energy Commission’s Public Interest Energy Research (PIER) Program.

Emissions from LFG recovery systems are assumed to be continuous and unvarying throughout the year.  The statewide quantity of flared LFG is apportioned to the county level according to the total tonnage of waste landfilled in each county over 1990 through 2000.  Note that Attachment B presents disposal tonnage estimates for a longer period, 1970 through 2000.  However, it was thought that newer landfills, which still are accepting wastes, are more likely to have LFG recovery systems because they are more likely to be subject to a New Source Performance Standards (NSPS) regulation, which was enacted March 1, 1996.  This regulation requires air emission reductions at new and existing landfills that currently accept wastes (EPA, 1998).

### Example Calculations

Emissions for gas-to-energy landfills are calculated from the estimated quantity of methane that is captured at these facilities.  Methane generation for each landfill was estimated according to the methods presented in Attachment B (Waste Disposal).  The EPA (1998) estimates that LFG recovery rates typically vary between 60 to 85 % of the total LFG generation rate.  A recovery rate of 85% is assumed for the example below, which was carried out for the Sacramento City Landfill.

47 MMscf/year ( 0.85 = 40 MMscf recovered/year (Sacramento)

40 MMscf recovered/year ( 18 lb SO2 /MMscf landfill gas ÷ 2000

= 0.36 tons SO2/year (Sacramento)

40 MMscf recovered/year ( 56 lb NOx /MMscf landfill gas ÷ 2000

= 1.1 tons NOx /year (Sacramento)

The results of similar calculations for other pollutants and other counties are listed in Table 2.  These emissions are assigned to the Resource Recovery emissions source category (CES no. 83055).

Table 2.   Annual missions for landfill gas-to-energy (LFGTE) facilities.

| Landfill Name | County | SO2 (tons) | NOx (tons) | CO (tons) | TOC (tons) | VOC (tons) | PM (tons) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Union Mine Disposal Site | El Dorado | 0.85 | 2.6 | 8.3 | 36 | 0.24 | 0.04 |
| Sacramento County Landfill (Kiefer) | Sacramento | 0.36 | 1.1 | 3.5 | 15 | 0.10 | 0.02 |
| Sacramento City Landfill | Sacramento | 3.8 | 12 | 37.1 | 161 | 1.1 | 0.19 |
| Yolo County Central Landfill | Yolo | 15 | 47 | 147 | 639 | 4.4 | 0.77 |

Statewide emissions from flared LFG are apportioned to counties according to the quantities of landfill wastes disposed at non-LFGTE facilities from 1990-2000 in each county.  Emissions from flared LFG are estimated below for Sacramento County.

1,197,236 tons waste landfilled (Sacramento) ÷ 271,157,808 tons waste landfilled (California) = 0.0044 Sacramento’s proportion of California total waste landfilled

0.0044 ( 15,000 MMscf flared (California) = 66 MMscf flared (Sacramento)

66 MMscf ( 7.9 lb SO2 /MMscf ÷ 2000 = 0.26 tons SO2 (Sacramento)

Table 3 presents the results of similar calculations for other counties.  These emissions are assigned to the Municipal Waste Disposal source category (CES no. 57281).

Table 3.  Annual emissions due to flared LFG.

| County | Proportion of State Waste Landfilled* | Methane Flared (MMscf) | SO2 (tons) | NOx (tons) | CO (tons) | TOC (tons) | PM (tons) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Amador | 0.1% | 15.5 | 0.06 | 0.03 | 0.6 | 1.0 | 0.01 |
| Butte | 0.7% | 99.9 | 0.39 | 0.20 | 3.7 | 6.3 | 0.08 |
| Calaveras | 0.1% | 18.0 | 0.07 | 0.04 | 0.7 | 1.1 | 0.02 |
| Colusa | 0.0% | 3.4 | 0.01 | 0.01 | 0.1 | 0.2 | 0.00 |
| El Dorado | 0.0% | 0.0 | 0.00 | 0.00 | 0.0 | 0.0 | 0.00 |
| Glenn | 0.1% | 13.0 | 0.05 | 0.03 | 0.5 | 0.8 | 0.01 |
| Mariposa | 0.0% | 7.0 | 0.03 | 0.01 | 0.3 | 0.4 | 0.01 |
| Mendocino | 0.2% | 32.3 | 0.13 | 0.06 | 1.2 | 2.0 | 0.03 |
| Nevada | 0.0% | 5.4 | 0.02 | 0.01 | 0.2 | 0.3 | 0.00 |
| Placer | 0.1% | 10.6 | 0.04 | 0.02 | 0.4 | 0.7 | 0.01 |
| Plumas | 0.0% | 4.3 | 0.02 | 0.01 | 0.2 | 0.3 | 0.00 |
| Sacramento | 0.4% | 65.5 | 0.26 | 0.13 | 2.5 | 4.1 | 0.06 |
| Shasta | 0.8% | 124.9 | 0.49 | 0.25 | 4.7 | 7.9 | 0.11 |
| Sierra | 0.0% | 1.6 | 0.01 | 0.00 | 0.1 | 0.1 | 0.00 |
| Solano | 1.6% | 241.7 | 0.95 | 0.48 | 9.1 | 15.3 | 0.21 |
| Tehama | 0.2% | 23.8 | 0.09 | 0.05 | 0.9 | 1.5 | 0.02 |
| Tuolumne | 0.1% | 7.8 | 0.03 | 0.02 | 0.3 | 0.5 | 0.01 |
| Yolo | 0.0% | 6.3 | 0.02 | 0.01 | 0.2 | 0.4 | 0.01 |
| Yuba | 0.6% | 89.0 | 0.35 | 0.18 | 3.3 | 5.6 | 0.08 |
| Alameda | 3.8% | 570.6 | 2.25 | 1.14 | 21.4 | 36.1 | 0.48 |
| Contra Costa | 2.1% | 316.1 | 1.25 | 0.63 | 11.9 | 20.0 | 0.27 |
| Del Norte | 0.1% | 8.8 | 0.03 | 0.02 | 0.3 | 0.6 | 0.01 |
| Fresno | 2.7% | 404.1 | 1.60 | 0.81 | 15.2 | 25.6 | 0.34 |
| Humboldt | 0.4% | 55.7 | 0.22 | 0.11 | 2.1 | 3.5 | 0.05 |
| Imperial | 0.6% | 94.1 | 0.37 | 0.19 | 3.5 | 6.0 | 0.08 |
| Inyo | 0.1% | 8.6 | 0.03 | 0.02 | 0.3 | 0.5 | 0.01 |
| Kern | 3.1% | 460.6 | 1.82 | 0.92 | 17.3 | 29.2 | 0.39 |
| Kings | 0.4% | 63.5 | 0.25 | 0.13 | 2.4 | 4.0 | 0.05 |
| Lake | 0.2% | 27.1 | 0.11 | 0.05 | 1.0 | 1.7 | 0.02 |
| Lassen | 0.1% | 10.6 | 0.04 | 0.02 | 0.4 | 0.7 | 0.01 |
| Los Angeles | 33.1% | 4906.5 | 19.38 | 9.81 | 184.0 | 310.6 | 4.17 |
| Madera | 0.3% | 49.3 | 0.19 | 0.10 | 1.8 | 3.1 | 0.04 |
| Marin | 0.0% | 5.2 | 0.02 | 0.01 | 0.2 | 0.3 | 0.00 |
| Merced | 0.8% | 114.5 | 0.45 | 0.23 | 4.3 | 7.2 | 0.10 |
| Modoc | 0.0% | 0.5 | 0.00 | 0.00 | 0.0 | 0.0 | 0.00 |
| Mono | 0.1% | 8.4 | 0.03 | 0.02 | 0.3 | 0.5 | 0.01 |
| Monterey | 0.2% | 32.7 | 0.13 | 0.07 | 1.2 | 2.1 | 0.03 |
| Napa | 0.5% | 74.0 | 0.29 | 0.15 | 2.8 | 4.7 | 0.06 |
| Orange | 7.3% | 1077.4 | 4.26 | 2.15 | 40.4 | 68.2 | 0.92 |
| Riverside | 5.8% | 859.9 | 3.40 | 1.72 | 32.2 | 54.4 | 0.73 |
| San Benito | 0.2% | 31.5 | 0.12 | 0.06 | 1.2 | 2.0 | 0.03 |
| San Bernardino | 5.9% | 877.9 | 3.47 | 1.76 | 32.9 | 55.6 | 0.75 |
| San Diego | 7.7% | 1140.7 | 4.51 | 2.28 | 42.8 | 72.2 | 0.97 |
| San Joaquin | 3.2% | 471.0 | 1.86 | 0.94 | 17.7 | 29.8 | 0.40 |
| San Luis Obispo | 0.9% | 129.3 | 0.51 | 0.26 | 4.8 | 8.2 | 0.11 |
| San Mateo | 3.6% | 536.6 | 2.12 | 1.07 | 20.1 | 34.0 | 0.46 |
| Santa Barbara | 1.8% | 259.8 | 1.03 | 0.52 | 9.7 | 16.4 | 0.22 |
| Santa Clara | 5.2% | 764.2 | 3.02 | 1.53 | 28.7 | 48.4 | 0.65 |
| Santa Cruz | 0.6% | 94.3 | 0.37 | 0.19 | 3.5 | 6.0 | 0.08 |
| Siskiyou | 0.1% | 12.5 | 0.05 | 0.02 | 0.5 | 0.8 | 0.01 |
| Sonoma | 0.0% | 2.6 | 0.01 | 0.01 | 0.1 | 0.2 | 0.00 |
| Stanislaus | 0.5% | 75.1 | 0.30 | 0.15 | 2.8 | 4.8 | 0.06 |
| Trinity | 0.0% | 4.0 | 0.02 | 0.01 | 0.1 | 0.3 | 0.00 |
| Tulare | 1.3% | 188.7 | 0.75 | 0.38 | 7.1 | 11.9 | 0.16 |
| Ventura | 2.2% | 322.9 | 1.28 | 0.65 | 12.1 | 20.4 | 0.27 |
| Total | 100% | 15,000 | 59 | 30 | 556 | 939 | 13 |

* at non-LFGTE facilities

## Solid Waste Combustion

Waste-to-energy facilities incinerate municipal solid waste (MSW) or biomass waste.  Biomass, or green waste, primarily is comprised of wood products.  Table 4 lists emission factors for wood residue combustion.  Wood heating values, which are in the range 4,500 to 8,000 MMBtu per pound of waste, are available from EPA (2001b).  The wood heating values are needed to convert the mass of waste throughput to the units that are required for application of the emission factors in Table 4.

Table 4.  Emission factors for combustion of wood residue in boilers (EPA, 2001b).a

| Wood Residue Combustion | NOx b | SO2 | CO | TOC | VOC | PM c | PM10 c |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Uncontrolled | 0.49 | 0.025 | 0.60 | 0.06 | 0.038 | 0.56 | 0.50 |
| PM control: fabric filter d | 0.49 | 0.025 | 0.60 | 0.06 | 0.038 | 0.1 | 0.074 |

a  The emission factors are in units of lbs pollutant/MMBtu.  These can be converted to units of lbs pollutant/ton wood waste by using a conversion rate of  HHV (  2000 MMBtu/ton wood, where HHV is the high wood heating value.  HHV depends on the type of waste (bark, shavings, sawdust, trimmings, etc.) and the moisture content (wet or dry).  (See EPA, 2001b)

b  The emission factor for NOx declines to 0.22 lbs/MMBtu when wet wood products are used as fuel.

c  The emission factors for PM and PM10 are conservatively high.  Emissions of PM depend on the type and condition of the wood fuel.  Dry wood and wet wood without bark produce less PM emissions.

d EPA (2001b) presents many alternative PM emission factors for various control technologies.  Fabric filters were assumed for this presentation.  If information regarding site-specific controls is available, consult EPA (2001b) to select the most appropriate emission factors case-by-case.

MSW incineration is conducted at three facilities that are permitted by the Integrated Waste Management Board (IWMB) and possibly a few additional other facilities in Southern California (US Census Bureau, 2001).  None of these MSW incineration facilities are located in CCOS II participating counties.  Table 5 lists waste-to-energy facilities that incinerate green waste.  Currently, the IWMB is developing a project to ascertain process rates for these facilities.  Mr. Howard Levenson is the contact for the IWMB research project.  However, no throughput data currently are available for this emissions source.  When the IWMB project is complete, emissions for this source should be estimated by applying suitable emission factors to the quantified waste throughput rates.  Emissions for this source should be assigned to the Resource Recovery emissions source category (EIC 099-080-0012-0000; CES no. 83055).

Table 5.   List of facilities that combust wood waste for energy conversion in the CCOS counties (Judd, 2001).

| County | Company Name | Location | Mailing Address | City | ZIP Code | Telephone Number | Contact Name |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Amador | Wheelabrator Environmental | Martell | 20811 Industry Road | Anderson | 96007 | (530) 378-5615 | Bill Carlson |
| Butte | Covanta Energy | Oroville | 3086 Crossroads Dr. | Redding | 96003 | (530) 224-3305 | Paul Wood |
| Colusa | Wadham Energy | Williams | 2420 Camino Ramon #101 | San Ramon | 94583 | (925) 244-1100 | Alex Sugaoka |
| Mendocino | Georgia Pacific | Fort Bragg | 90 West Redwood | Fort Bragg | 95437 | (707) 961-3272 | Ron Holen |
| Placer | Rio Bravo/ Constellation | Rocklin | 1201 Dove Street #470 | Newport Beach | 92660 | (949) 852-0606 | Bob Escalante |
| Placer | Sierra Pacific Industries | Lincoln | PO Box 496011 | Redding | 96049 | (530) 378-8179 | Bob Ellery |
| Plumas | Collins Pine | Chester | 1618 SW First Ave. #500 | Portland, OR | 97201 | (503) 227-1219 | Wade Mosby |
| Plumas | Sierra Pacific Industries | Quincy | PO Box 496011 | Redding | 96049 | (530) 378-8179 | Bob Ellery |
| Shasta | Burney Forest Power | Burney | 35586-B Highway 299 East | Burney | 96013 | (530) 335-5100 | Milt Schultz |
| Shasta | Covanta Energy | Burney | 3085 Crossroads Dr. | Redding | 96003 | (530) 224-3305 | Paul Wood |
| Shasta | Sierra Pacific Industries | Burney | PO Box 496011 | Redding | 96049 | (530) 378-8179 | Bob Ellery |
| Shasta | Wheelabrator Environmental | Anderson | 20811 Industry Road | Anderson | 96007 | (530) 378-5615 | Bill Carlson |
| Shasta | Wheelabrator Environmental | Hudson | 20811 Industry Road | Anderson | 96007 | (530) 378-5615 | Bill Carlson |
| Sierra | Sierra Pacific Industries | Loyalton | PO Box 496011 | Redding | 96049 | (530) 378-8179 | Bob Ellery |
| Tuolumne | Pacific Ultrapower | Chinese Station | 8755 Enterprise Dr. | Jamestown | 95327 | (209) 984-4660 | Chris Trott |
| Tuolumne | Sierra Pacific Industries | Sonora | PO Box 496011 | Redding | 96049 | (530) 378-8179 | Bob Ellery |
| Yolo | Thermo Ecotek Corp | Woodland | Not Available |  |  |  |  |

## References

EPA (2001a) Inventory of U.S. greenhouse gas emissions and sinks 1990-1999, Chapter 7, Waste.  Report prepared by Office of Air Quality Planning and Standards of the EPA, Research Triangle Park, NC.

EPA (2001b) Wood Residue Combustion in Boilers.  In compilation of air pollutant emission factors, vol. 1: stationary point and area emission units (AP-42), 5th ed. (January 1995), Chapter 1.6.  Report prepared by Office of Air Quality Planning and Standards of the EPA, Research Triangle Park, NC.

EPA (2001c) Landfill Methane Outreach Program. Database maintained by the US Environmental Protection Agency, Research Triangle Park, NC, and accessed November 2001 at web site http://www.epa.gov/lmop/projects/projects.htm.

EPA (2000) Stationary Gas Turbines.  In compilation of air pollutant emission factors, vol. 1: stationary point and area emission units (AP-42), 5th ed. (January 1995), Chapter 3.1.  Report prepared by Office of Air Quality Planning and Standards of the EPA, Research Triangle Park, NC.

EPA (1999) Volatile organic compound/particulate matter speciation database management system (SPECIATE), version 3.1 (for microcomputers).  Prepared by the Office of Air Quality Planning and Standards, U.S. Environmental Protection Agency, Research Triangle Park, NC October.

EPA (1998) Municipal Solid Waste Landfills.  In compilation of air pollutant emission factors, vol. 1: stationary point and area emission units (AP-42), 5th ed. (January 1995), Chapter 3.1.  Report prepared by Office of Air Quality Planning and Standards of the EPA, Research Triangle Park, NC.

Judd, B. (2001)  Personal communication.  Director of the California Biomass Energy Alliance, Sacramento, California.  Telephone (916) 444-8333.

Levenson, H. (2001)  Personal communication.  California Integrated Waste Management Board, Sacramento, California.  Telephone (916) 341-6583.

US Census Bureau (2001) Censtats databases: county business patterns data.  Database maintained by the US Census Bureau, Washington, D.C., and accessed December 2001 at web site http://tier2.census.gov/dbappweb.htm.