Relationships Among Organic Gas Terms

Used in the Emission Inventory

MOTOR VEHICLES:

1.  NMHC    	+	methane	=	HC     		[or THC

(non-methane                     	     (hydrocarbons)         		 total hydrocarbons]

hydrocarbons)

-- NMHC and HC (THC) contain only hydrocarbons (not oxygenated compounds

like aldehydes) due to GC-FID measurement technique

-- NMHC and HC must be adjusted for the oxygenated compounds to get NMOG

2.  NMHC 		----------> 		NMOG

(non-methane     	adjust to add     	(non-methane organic gas)

hydrocarbons)   	oxygenated cmpds

3. NMOG      	+   	methane    	= 	~  TOG

(non-methane                			approximately  Total Organic Gas

organic gas)

OVERALL INVENTORY:

4. TOG      	x    		FROG  			=	ROG

(Fraction of Reactive Organic Gas) 	(Reactive Organic Gas)

5. TOG	x		FR_VOC 		=	VOC

(Fraction of Volatile Organic Cmpds)         	(Volatile Organic Cmpds)

-- VOC is U.S. EPA term -- uses a separate federal list of exempted cmpds

6. TOG	-	Exempt cmpds			=	ROG

[ ARB list of methane,

ethane, CFCs, etc.]

===================================================================

ARB / 7-00