## Slide 1: Enhanced Stage II Vapor Recovery and Storage Tank Evaporative Emissions
Ted Tiberi
ARID Technologies, Inc.
www.ARIDtech.com
630.681.8500
ttiberi@ARIDtech.com

## Slide 2: Outline
Review of Storage Tank Evaporative Loss Dynamics
Section 4.1 of CP-201
  Emission Factor <= 0.38 lb/1,000 gal
    Fugitive Emissions <= 50% of this value, or 0.19 lb/1,000 gal
Section 4.6 of CP-201
  Daily Avg <= 0.25 iwc
  Daily High <= 1.50 iwc
TP-201.2 F, Section 9, Table 9.1
  Use this format to tabulate fugitive emission factor
  Combine the fugitive emission factor with site throughput to calculate mass emissions

## Slide 3: Outline (cont’d.)
Based on capital and operating expense of control options, tabulate a cost effectiveness in $/lb or $/ton of VOC emissions reduced
With use of a benzene concentration level, based on a relevant observed hydrocarbon concentration of emitted vapors, tabulate a benzene emission factor
With guidance from “Scoping Plan”, consider designated levels for attaining and maintaining ambient air quality standards and acceptable risk levels for toxic exposure
Apply emission thresholds and cost effectiveness to range of GDF; for example GDF 1, 2, 3, 4, 5; with average throughput of 25 k gal, 37.5, 75, 150, and 300 k gal/month

## Slide 4: The Uncontrolled System
ARID TECHNOLOGIES, INC. 2020

## Slide 5
Uncontrolled System

## Slide 6
Uncontrolled System

## Slide 7
Uncontrolled System

## Slide 8
Uncontrolled System

## Slide 9
0
-
+
Uncontrolled System

## Slide 10
0
-
+
Uncontrolled System

## Slide 11
% HC, P/V ON

## Slide 12: Stage II Recovery Systems

## Slide 13: Stage II Recovery Systems
Balanced System
Vacuum-Assisted System

## Slide 14: Stage II Recovery Systems
Balanced System
Vacuum-Assisted System

## Slide 15
0
-
+
Vacuum-Assisted Recovery Systems

## Slide 16
0
-
+
Vacuum-Assisted Recovery Systems

## Slide 17
0
-
+
Vacuum-Assisted Recovery Systems

## Slide 18
0
-
+
Vacuum-Assisted Recovery Systems

## Slide 19
0
-
+
Vacuum-Assisted Recovery Systems

## Slide 20: ORVR Configuration
Enhanced Evap/ORVR Canister
Vapor Line
Shut-off Valve
Check Valve
Pressure Relief Valve

## Slide 21
ORVR Systems

## Slide 22
ORVR Systems

## Slide 23
ORVR Systems

## Slide 24
0
-
+
ORVR Systems

## Slide 25
0
-
+
ORVR Systems

## Slide 26: Permeator™ Systems

## Slide 27: Permeator™ Systems

## Slide 28: Permeator™ Systems
0
-
+

## Slide 29: Permeator™ Systems
0
-
+

## Slide 30: Permeator™ Systems
0
-
+

## Slide 31: Permeator™ Systems
0
-
+

## Slide 32: Permeator™ Systems
0
-
+

## Slide 33: Permeator™ Systems
0
-
+
0
-
+

## Slide 34
0
-
+
Groundwater Contamination

## Slide 35
Non Stage II Site w/Permeator
Atlanta, GA

## Slide 36
Non Stage II Site w/Permeator
Atlanta, GA

## Slide 37
460 Chula Vista

## Slide 38
460 Chula Vista

## Slide 39
HEALY CAS, No PERMEATOR

## Slide 40
471 Cal Expo

## Slide 41
471 Cal Expo

## Slide 42
Chart: Cal Expo 471: Pressure Profile 12 NOV - 15 DEC 2014 CAS and No Permeator
| 0 -.25 | .26 - .50 | .51 - .75 | .76 - 1.00 | 1.01 - 1.25 | 1.26 - 1.50 | 1.51 - 1.75 | 1.76 - 2.00 | 2.01 - 2.25 | 2.26 - 2.50 | 2.51 - 3.00 | 3.01 - 4.25 | <0 | >4.25
 | 0.017267 | 0.050044 | 0.050086 | 0.035328 | 0.029767 | 0.026673 | 0.015762 | 0.017267 | 0.017308 | 0.022618 | 0.022367 | 0.054308 | 0.62657 | 8.3616e-05

## Slide 43
Table 9.1 |  |  |  |  | Equ 9.2.1 |  | Equ 9.2.2 |  | Equ 9.3.1 |  |  |  | Equ 9.4.1
cfm | P range value |  | minutes |  | V (ft3) |  | Q (CFH) |  | M | C | MW | MV | E (lbm/1,000 gal)
0.005254688 | 0.125 |  | 825.97 |  | 4.340190414 |  |  |  | lbm/hr |  |  |  | 
0.05024674 | 1.13 |  | 1423.94 |  | 71.54836636 |  |  |  |  |  |  |  | 
0.07666982 | 2.13 |  | 827.97 |  | 63.47995689 |  |  |  |  |  |  |  | 
0.0203118 | 0.38 |  | 2393.90 |  | 48.62441624 |  |  |  |  |  |  |  | 
0.05770824 | 1.38 |  | 1275.95 |  | 73.6326357 |  |  |  |  |  |  |  | 
0.08236432 | 2.38 |  | 1081.95 |  | 89.11446841 |  |  |  |  |  |  |  | 
0.03248555 | 0.63 |  | 2395.90 |  | 77.83212368 | ft3 |  |  |  |  |  |  | 
0.06449474 | 1.63 |  | 753.97 |  | 48.62700089 |  |  |  |  |  |  |  | 
0.09049328 | 2.76 |  | 1069.96 |  | 96.82376145 |  |  |  |  |  |  |  | 
0.0420968 | 0.88 |  | 1689.93 |  | 71.14061765 |  |  |  |  |  |  |  | 
0.07060624 | 1.88 |  | 825.97 |  | 58.31831598 |  |  |  |  |  |  |  | 
0.10671182 | 3.63 |  | 2597.89 |  | 277.2257177 |  |  |  |  |  |  |  | 
 |  |  |  | V total | 980.7075713 |  | 1.230087262 |  | 0.050478192 | 36 | 44 | 386 | 0.242683617
 |  |  |  |  | 980.7075713 |  | 1.230087262 |  | 0.064499912 | 46 | 44 | 386 | 0.310095733

## Slide 44: Healy CAS Fugitive Emissions
E = 0.31 lb/1,000 gal
Daily Avg <= 0.25 iwc; 85% Failure Rate
Daily High <= 1.50 iwc; 78 % Failure Rate
75th percentile of 30 day pressue = +0.75 iwc
  Failed 0.3 iwc limit
Are Fugitives > 50% of Overall Emission Factor?
  .50 x 0.38 = 0.19 lb/1,000 gal
  YES; system does not meet CARB Specifications for Certification

## Slide 45
Chart: Cal Expo 471: Pressure Profile 17 DEC 2014 - 19 JAN 2015 with PERMEATOR (CAS Removed)
| 0 -.25 | .26 - .50 | .51 - .75 | .76 - 1.00 | 1.01 - 1.25 | 1.26 - 1.50 | 1.51 - 1.75 | 1.76 - 2.00 | 2.01 - 2.25 | 2.26 - 2.50 | 2.51 - 3.00 | 3.01 - 4.25 | <0 | >4.25
 | 0.26645 | 0.10325 | 0.00075304 | 0.00012551 | 0 | 4.1836e-05 | 0 | 0 | 0 | 4.1836e-05 | 4.1836e-05 | 0 | 0.61432 | 0.00012551

## Slide 46
Table 9.1 | P range value |  |  |  | Equ 9.2.1 |  | Equ 9.2.2 |  | Equ 9.3.1 |  |  |  | Equ 9.4.1
cfm |  |  | minutes |  | V (ft3) |  | Q (CFH) |  | M | C | MW | MV | E (lbm/1,000 gal)
0.005254688 | 0.125 |  | 12737.47 |  | 66.93140913 |  |  |  | lbm/hr |  |  |  | 
0.05024674 | 1.13 |  | 0.00 |  | 0 |  |  |  |  |  |  |  | 
0.07666982 | 2.13 |  | 0.00 |  | 0 |  |  |  |  |  |  |  | 
0.0203118 | 0.38 |  | 4935.79 |  | 100.2548504 |  |  |  |  |  |  |  | 
0.05770824 | 1.38 |  | 2.00 |  | 0.115411651 |  |  |  |  |  |  |  | 
0.08236432 | 2.38 |  | 2.00 |  | 0.164721748 |  |  |  |  |  |  |  | 
0.03248555 | 0.63 |  | 36.00 |  | 1.169430874 |  |  |  |  |  |  |  | 
0.06449474 | 1.63 |  | 0.00 |  | 0 |  |  |  |  |  |  |  | 
0.09049328 | 2.76 |  | 2.00 |  | 0.180978988 |  |  |  |  |  |  |  | 
0.0420968 | 0.88 |  | 0.10 |  | 0.004209504 |  |  |  |  |  |  |  | 
0.07060624 | 1.88 |  | 0.00 |  | 0 |  |  |  |  |  |  |  | 
0.10671182 | 3.63 |  | 0.00 |  | 0 |  |  |  |  |  |  |  | 
 |  |  |  | V total | 168.8210123 | ft3 | 0.211891489 |  | 0.008695236 | 36 | 44 | 386 | 0.04180402
 |  |  |  |  |  |  | 0.211891489 |  | 0.01111058 | 46 | 44 | 386 | 0.053416248

## Slide 47: ARID Permeator Fugitive Emissions
E = 0.053 lb/1,000 gal
Daily Avg <= 0.25 iwc; 0% Failure Rate
Daily High <= 1.50 iwc; 0 % Failure Rate
75th percentile of 30 day pressue = +0.18 iwc
  Passed 0.3 iwc limit
Are Fugitives > 50% of Overall Emission Factor?
  .50 x 0.38 = 0.19 lb/1,000 gal
  NO; system meets CARB Specifications for Certification

## Slide 49
Are benzene weight % values accurate considering
Elevated vapor concentration of hydrocarbon emissions?

## Slide 50: Fugitive Emission Factor as Basis for Mass Emission Rate at Specific GDF
Fugitive Emission Factor (lb/1,000 gal), E
E x GDF Throughput/month = lb/month
Threshold and Cost Effectiveness Determined by ARB
  Monthly VOC Emission Limit
  Monthly Benzene Emission Limit
  Costs per Ton of VOC reduced
ARB can develop requirements to GDF based on throughput range
  For example GDF1, GDF2, GDF3, GDF4, GDF5 for throughputs of 25 k gal, 37.5 , 75, 150, and 300 k gal

## Slide 51: IT Backbone/Infrastructure
Internet enabled ISD systems provided by Veeder-Root and Franklin Fueling Systems are presently in widespread use throughout CA
ISD raw data acquisition in place as percentile metrics are presently calculated daily
The percentile calculations can be augmented or replaced by the pressure interval calculations
  The Pressure Interval metrics are subsequently used to calculate fugitive emission factors
    The fugitive emission factors are then used to tabulate absolute, site specific emissions levels which are the product of (Emission Factor) x Throughput

## Slide 52: Modification of ISD to include fugitive and vent emission rates
Seems like an incremental investment to include simple programming within the ISD systems provided by Veeder-Root and Franklin Fueling Systems
Pressure data is important, but at present, these metrics are “stand-alone”
Key is to use existing pressure data to calculate emission rates, both fugitive and vent
The emission rates are then combined with site throughput to yield meaningful and useful metrics for ARB to use in their focused rulemaking