## Slide 1: Energy Targets and Performance Specifications SMUD House of the Future
September 10, 2007
Dr. Ren Anderson, NREL
Hot Dry Climate Region

## Slide 2: Agenda
Introduction
Process Overview
Energy Performance Goals
Target Performance Specs
Brainstorm Green Goals
Other Participants
Publicity
Project Requirements
Wrap-up/Next Steps

## Slide 3: Process Overview and Planning Schedule
Today: Base Energy Performance Specs
Three Weeks: Emerging Energy Savers (MEL’s, demand/response, …)
Six Weeks: Green Materials

## Slide 4: Energy Performance Goals
Annual Source Energy: 80% Reduction
Zero Net Summer Peak Electric Demand: 4 PM to 8 PM
(2500 ft2 floor area target)

## Slide 5: NREL Reference House
2400 SF, 3 Bdrm, 2 Ba
16% Glazing
Back Facing West
4 Occupants

## Slide 6
HOF Base Energy Performance Specs
2x6/R19-R21 cavity/R12 insulating sheathing (R30 wall assembly)
R50 ceiling assembly
Tight Envelope, .0002 SLA (4 ACH50)
Low e/low SHGC glazing (0.3 U-value, 0.26 SHGC)
90% CFL Lighting
SEER 18+ AC/Freus/3 ton with 4-8 PM summer setup
AFUE 90+ furnace
Solar hot water with tankless gas hot water backup, (EF 0.80+)
Tight ducts, inside conditioned space (mastic, 5% leakage)
Gas clothes dryer
4.5kW PV
Energy Star Appliances
Estimated cost increase relative to standard home2,3: +$20.00/ft2
Notes:
1. Equivalent packages may be substituted, based on specific builder preferences
2. Incremental costs estimated relative to minimum T-24

## Slide 7: Annual Energy, End Uses
T24
HOF
PV

## Slide 8: Current SMUD Results

## Slide 9: Peak Demand: HOF Base, 4kWac West Array
T24
HOF

## Slide 10
This work has been authored by an employee or employees of the Midwest Research Institute under Contract No. DE-AC36-99GO10337 with the U.S. Department of Energy. The United States Government retains and the publisher, by accepting the article for publication, acknowledges that the United States Government retains a non-exclusive, paid-up, irrevocable, worldwide license to publish or reproduce the published form of this work, or allow others to do so, for United States Government purposes.

## Slide 11: Net Annual Operating Cost, Without Incentives