Attachment:  Modified Proposed Regulation Order

The following text shows the Board-approved modifications to the originally proposed regulatory text for section 2011, title 13, California Code of Regulations.  The modifications to the regulatory language approved at the March 24, 2004 public hearing and made available during the first comment period ending January 7, 2005, are shown in underline to indicate additions and strikethrough to indicate deletions.  The modifications presented in this document are shown in double underline to indicate additions and double strikethrough to indicate deletions.  No other regulatory sections affected by the March 24, 2004 approval are proposed for modification herein.

Adopt new section 2011, title 13, California Code of Regulations to read as follows:  (Note:  the entire text of section 2011 as set forth and modified below, is new language proposed to be added to the California Code of Regulations.)

§ 2011.  Software Upgrade for 1993 through 1998 Model Year Heavy-Duty Trucks.

- Applicability.  This section 2011 applies to Low NOx Rebuild Engines, as defined, operating in the State of California that are either;

(1)	registered in California; or

(2)	registered outside of California, as defined.

- Definitions.  The definitions in section 1900 (b), Chapter 1, title 13 of the California Code of Regulations apply, with the following additions:

- “Driver” has the same meaning as title 13, California Code of Regulations, section 2180.1 (a)(7).

(2)	“HHDDE” means a heavy-duty diesel engine certified as a motor vehicle heavy heavy-duty engine in accordance with title 13, California Code of Regulations, section 1956.8.

(3) 	“Incentive project” means a project conducted under applicable provisions in part IX.C of the Heavy Duty Diesel Engine Settlement Agreements with California and Consent Decrees with the United States Environmental Protection Agency.  The California Settlement Agreements and federal Consent Decrees are identified in title 13, California Code of Regulations, section 1956.8 (a)(2)(A), footnote 1.

(4)	“Low NOx Rebuild Kit” means an engine manufacturer’s software and/or minor hardware upgrade that results in lower emissions of oxides of nitrogen (NOx) when installed on the engine control module of heavy-duty diesel engines requiring such kits.  Such engines are identified in plans implementing a Low NOx Rebuild Program under both Heavy Duty Diesel Engine Settlement Agreements with California and Consent Decrees with the United States Environmental Protection Agency, and are listed in (b)(5).  The California Settlement Agreements and federal Consent Decrees are identified in title 13, California Code of Regulations, section 1956.8 (a)(2)(A), footnote 1.

(5)	“Low NOx Rebuild Engine” means a 1993 through 1998 model year heavy-duty diesel engine for which a Low NOx Rebuild Kit must be available for installation.  The complete list of Low NOx Rebuild Engines is:

| Low NOx Rebuild Engines |
| --- |
| Make and Year | Engine Model | Notes |
| Caterpillar 19934 – 1998 | 3406E | Engine Serial Number (ESN) 5EK05767 and up through 5EK99381 |
| Caterpillar 19934 – 1998 | 3406E | ESN: 6TS00097 and up through 6TS27803 |
| Caterpillar 19934 – 1998 | 3406E | ESN: 1LW00001 through 1LW33262 |
| Caterpillar 19934 – 1998 | 3406E | ESN: Reman 4AS00001 through 4AS00385 |
| Caterpillar 19935 – 1998 | 3126 | ESN: 1WM00210 through 1WM26819 |
| Caterpillar 19935 – 1998 | 3126 | ESN: 4ES000226 through 4ES00454 |
| Caterpillar 19935 – 1998 | 3126 | ESN: Reman 6RW00001 and up |
| Caterpillar 1993 – 1998 | 3126B | ESN: 7AS00001 through 7AS375882636 |
| Caterpillar 19935 – 19987 | 3116 | ESN: 8WL00297 through 8WL07351 |
| Caterpillar 1993 – 1998 | 3176B | ESN: 9CK00647 through 9CK32795 |
| Caterpillar 1993 – 1998 | 3176B | ESN: Reman 3LZ00001 and up |
| Caterpillar 1993 – 1998 | C-10 | ESN: 2PN01000 through 2PN07278 |
| Caterpillar 1993 – 1998 | C-10 | ESN: 8YS00449 through 8YS07060 |
| Caterpillar 1993 – 1998 | C-10 | ESN: Reman AKB00001 and up |
| Caterpillar 1993 – 1998 | C-12 | ESN: 1YN01200 through 1YN12844 |
| Caterpillar 1993 – 1998 | C-12 | ESN: 9NS00372 through 9NS19786 |
| Caterpillar 1993 – 1998 | C-12 | ESN: Reman ALS00001 and up |
| Cummins 1993 – 1998 | ISB Critical Parts List Number (CPL) 2446 | Critical Parts List Number (CPL) 2446 through 2451 |
|  |  | Horsepower (HP) | Torque (lb-ft) | Governed Speed | Original Software Calibration (SC) Options and Supercessions | Low NOx SC Option |
|  |  | 175 | 420 | 2500 | 9819 | 9819 |
|  |  | 175 | 420 | 2500 | 9845 | 9845 |
| Cummins 1993 – 1998 | ISB CPL 2447 | 190 | 520 | 2500 | 9818 | 9818 |
|  |  | 190 | 520 | 2500 | 9846 | 9846 |
|  |  | 195 | 520 | 2600 | 9817 | 9817 |
|  |  | 195 | 520 | 2600 | 9838 | 9838 |
| Cummins 1993 – 1998 | ISB CPL 2448 | 210 | 520 | 2600 | 9816 | 9816 |
|  |  | 210 | 520 | 2600 | 9852 | 9852 |
|  |  | 215 | 520 | 2500 | 9815 | 9815 |
|  |  | 215 | 520 | 2500 | 9847 | 9847 |
|  |  | 215 | 605 | 2500 | 9821 | 9821 |
|  |  | 215 | 605 | 2500 | 9850 | 9850 |
| Cummins 1993 – 1998 | ISB CPL 2449 | 230 | 605 | 2500 | 9814 | 9814 |
|  |  | 230 | 605 | 2500 | 9848 | 9848 |
|  |  | 230 | 660 | 2500 | 9820 | 9820 |
|  |  | 230 | 660 | 2500 | 9851 | 9851 |
| Cummins 1993 – 1998 | ISB CPL 2450 | 250 | 660 | 2500 | 9813 | 9813 |
|  |  | 250 | 660 | 2500 | 9849 | 9849 |
| Cummins 1993 – 1998 | ISB CPL 2451 | 275 | 660 | 2500 | 9812 | 9812 |
|  |  | 275 | 660 | 2500 | 9875 | 9875 |
| Cummins 1993 – 1998 | M11 CPL 1855 | CPL 1855, 1856, 1857, 2036, 2037, 2370, and 2371 |
|  |  | 330 | 1250 | 2000 | 2798, 2818, 2834, 2889, 2950, 2124, 2285, 2474, 2542 | 20234 |
|  |  | 330 | 1250 | 1800 | 2935, 2949, 2125, 2286, 2475, 2543 | 20235 |
|  |  | 310 | 1150 | 2000 | 2923, 2954, 2129, 2287, 2476, 2544 | 20236 |
|  |  | 310 | 1150 | 1800 | 2922, 2936, 2953, 2130, 2288, 2477, 2545 | 20237 |
|  |  | 280 | 1050 | 2000 | 2784, 2794, 2814, 2830, 2885, 2921, 2958, 2133, 2292, 2480, 2548 | 20238 |
|  |  | 280 | 1050 | 1800 | 2829, 2884, 2920, 2957, 2134, 2293, 2481, 2550 | 20239 |
|  |  | 280 ESP | 1050 | 1800 | 2792, 2883, 2928, 2961, 2181, 2298, 2391, 2485, 2556 | 20241 |
| Cummins 1993 – 1998 | M11 CPL 1856 | 370 | 1350 | 2000 | 2791, 2804, 2825, 2841, 2896, 2943, 2117, 2278, 2465, 2529 | 20228 |
|  |  | 370 | 1350 | 1800 | 2932, 2942, 2118, 2279, 2466, 2532 | 20229 |
|  |  | 350 | 1350 | 2000 | 2802, 2823, 2839, 2894, 2945, 2119, 2280, 2469, 2535 | 20230 |
|  |  | 350 | 1350 | 1800 | 2933, 2944, 2120, 2281, 2470, 2537 | 20231 |
|  |  | 330 | 1350 | 2000 | 2800, 2821, 2837, 2892, 2947, 2122, 2283, 2472, 2539 | 20232 |
|  |  | 330 | 1350 | 1800 | 2934, 2946, 2123, 2284, 2473, 2541 | 20233 |
| Cummins 1993 – 1998 | M11 CPL 1857 | 310 ESP | 1150 | 1800 | 2960, 2180, 2297, 2390, 2484, 2553 | 20240 |
| Cummins 1993 – 1998 | M11 CPL 2370 | 330 | 1250 | 1800 | 2601 | 20304 |
|  |  | 330 | 1250 | 1800 | 2598 | 20305 |
|  |  | 310 | 1150 | 2100 | 2603 | 20306 |
|  |  | 280 | 1050 | 1800 | 2605 | 20307 |
|  |  | 330 | 1250 | 2100 | 2599 | 20308 |
|  |  | 310 | 1150 | 1800 | 2602 | 20309 |
|  |  | 280 | 1050 | 1800 | 2604 | 20310 |
|  |  | 305 | 1150 | 2100 | 2698 | 20311 |
| Cummins 1993 – 1998 | M11 CPL 2371 | 370 | 1350 | 1800 | 2588 | 20312 |
|  |  | 350 | 1350 | 1800 | 2591 | 20313 |
|  |  | 350 | 1350 | 1800 | 2594 | 20314 |
|  |  | 330 | 1350 | 1800 | 2595 | 20315 |
|  |  | 370 | 1450 | 1800 | 2587 | 20316 |
|  |  | 330 | 1350 | 2100 | 2589 | 20317 |
|  |  | 330 | 1350 | 2100 | 2596 | 20318 |
|  |  | 420 | 1450 | 2100 | 2620 | 20319 |
|  |  | 370 | 1350 | 1800 | 2621 | 20320 |
|  |  | 370 | 1350 | 1800 | 2627 | 20321 |
|  |  | 335 | 1350 | 2100 | 2631 | 20322 |
| Cummins 1993 – 1998 | M11 CPL 2036 | 330 | 1250 | 1800 | 2264 | 20289 |
|  |  | 330 | 1250 | 1800 | 2261 | 20290 |
|  |  | 310 | 1150 | 2100 | 2266 | 20291 |
|  |  | 280 | 1050 | 2100 | 2268 | 20292 |
|  |  | 330 | 1250 | 2100 | 2262 | 20293 |
|  |  | 310 | 1150 | 1800 | 2265 | 20294 |
|  |  | 280 | 1050 | 1800 | 2267 | 20295 |
| Cummins 1993 – 1998 | M11 CPL 2037 | 400 | 1450 | 1800 | 2189 | 20296 |
|  |  | 370 | 1350 | 1800 | 2191 | 20297 |
|  |  | 350 | 1350 | 1800 | 2194 | 20298 |
|  |  | 350 | 1350 | 1800 | 2197 | 20299 |
|  |  | 330 | 1350 | 1800 | 2198 | 20300 |
|  |  | 370 | 1450 | 2100 | 2190 | 20301 |
|  |  | 370 | 1350 | 2100 | 2192 | 20302 |
|  |  | 370 | 1350 | 1800 | 2440 | 20303 |
| Cummins 1993 – 1998 | N14 CPL 1573 | CPL 1573, 1574, 1807, 1809, 1844, 1987, 2025, 2026, 2027, 2389, 2390, and 2391 |
|  |  | 370 | 1400 | 1800 | 1215, 1510, 1590, 10017 | 10469 |
|  |  | 370/460 ESP | 1400/ 1550 | 2100 | 1216, 1306, 1512, 1259, 1592, 10019 | 10470 |
|  |  | 410 | 1450 | 2100 | 1218, 1514, 1594, 10021 | 1047 |
|  |  | 430 | 1450 | 1800 | 1220, 1515, 1595, 10022 | 10472 |
|  |  | 430 | 1450 | 2100 | 1219, 1516, 1596, 10023 | 10473 |
| Cummins 1993 – 1998 | N14 CPL 1574 | 310 | 1250 | 1800 | 1204, 1501, 1581, 10008 | 10463 |
|  |  | 310/430 ESP | 1250/ 1450 | 1800 | 1206, 1304, 1502, 1567, 1582, 10009 | 10464 |
|  |  | 330 | 1350 | 1800 | 1207, 1503, 1583, 10010 | 10465 |
|  |  | 330 | 1350 | 1800 | 1125, 1208, 1504, 1584, 10011 | 10466 |
|  |  | 350 | 1350 | 1800 | 1211, 1507, 1587, 10014 | 10467 |
|  |  | 350 | 1400 | 1800 | 1212, 1508, 1588, 10015 | 10468 |
| Cummins 1993 – 1998 | N14 CPL 1807 | 310 | 1250 | 1800 | 1141, 1242, 1360, 1632, 10076 | 10480 |
|  |  | 310/390 ESP | 1250/ 1450 | 1800 | 1142, 1243, 1300, 1409, 1570, 1633, 10077 | 10481 |
|  |  | 330 | 1350 | 1800 | 1143, 1244, 1361, 1634, 10078 | 10482 |
|  |  | 330 | 1350 | 1800 | 1551, 1635, 10079 | 10483 |
|  |  | 330 | 1350 | 1800 | 1602, 1636, 10080 | 10484 |
|  |  | 330 | 1350 | 2100 | 1144, 1245, 1362, 1637, 10081 | 10485 |
|  |  | 350 | 1350 | 1800 | 1145, 1246, 1363, 1638, 10082 | 10486 |
|  |  | 350 | 1350 | 1800 | 1552, 1639, 10083 | 10487 |
|  |  | 350 | 1400 | 1800 | 1147, 1248, 1365, 1641, 10085 | 10488 |
|  |  | 350 | 1400 | 2100 | 1148, 1249, 1366, 1642, 10086 | 10489 |
|  |  | 350/390 ESP | 1350/ 1500 | 1800 | 1149, 1185, 1250, 1251, 1367, 1571, 1643, 10087 | 10490 |
|  |  | 370 | 1400 | 1800 | 1150, 1253, 1368, 1646, 10090 | 10491 |
|  |  | 370 | 1400 | 1800 | 1553, 1647, 10091 | 10492 |
|  |  | 370 | 1450 | 1800 | 1152, 1255, 1370, 1649, 10093 | 10493 |
|  |  | 370 | 1450 | 2100 | 1153, 1256, 1371, 1650, 10094 | 10494 |
| Cummins 1993 – 1998 | N14 CPL 1809 | 410 | 1450 | 1800 | 1163, 1258, 1373, 1655, 10099 | 10496 |
|  |  | 410 | 1450 | 1800 | 1555, 1656, 10100 | 10497 |
|  |  | 410 | 1450 | 2100 | 1164, 1259, 1374, 1657, 10101 | 10498 |
|  |  | 410 | 1450 | 2100 | 1556, 1658, 10102 | 10499 |
|  |  | 435 | 1450 | 1800 | 1165, 1260, 1375, 1659, 10103 | 10500 |
|  |  | 435 | 1450 | 2100 | 1100, 1166, 1261, 1376, 1661, 10105 | 10501 |
|  |  | 435 | 1450 | 2100 | 1578, 10045, 10106 | 10502 |
|  |  | 435 | 1550 | 1800 | 1101, 1167, 1262, 1377, 1662, 10107 | 10503 |
|  |  | 435 | 1550 | 2100 | 1102, 1168, 1263, 1378, 1663, 10108 | 10504 |
| Cummins 1993 – 1998 | N14 CPL 1844 | 400/460 ESP | 1450/ 1650 | 1800 | 1103, 1161, 1170, 1265, 1266, 1267, 1380, 1381, 1575, 1665, 10100 | 10505 |
|  |  | 435 | 1650 | 2100 | 1104, 1171, 1269, 1383, 1667, 10113 | 10506 |
|  |  | 460 | 1650 | 2100 | 1106, 1173, 1272, 1386, 1670, 10116 | 10507 |
|  |  | 500 | 1650 | 2100 | 1107, 1135, 1274, 1388, 1672, 10118 | 10508 |
| Cummins 1993 – 1998 | N14 CPL 1987 | 350/435 | 1350/ 1550 | 1800 | 1184, 1257, 1372, 1546, 1574, 1603, 1654, 10098 | 10495 |
| Cummins 1993 – 1998 | N14 CPL 2025 | 435 | 1450 | 1800 | 1437 | 10616 |
|  |  | 435 | 1450 | 2100 | 1438 | 10617 |
|  |  | 435 | 1550 | 1800 | 1439 | 10618 |
|  |  | 435 | 1550 | 2100 | 1440 | 10619 |
|  |  | 435 | 1650 | 1900 | 1542 | 10620 |
|  |  | 435 | 1650 | 2100 | 1442 | 10621 |
|  |  | 435/500 ESP | 1550/ 1650 | 2100 | 1455 | 10622 |
|  |  | 460 | 1550 | 2100 | 1444 | 10623 |
|  |  | 460 | 1650 | 1900 | 1538 | 10624 |
|  |  | 460 | 1650 | 2100 | 1446 | 10625 |
|  |  | 500 | 1650 | 2100 | 1447 | 10626 |
|  |  | 500 | 1750 | 2100 | 1448 | 10627 |
|  |  | 525 | 1850 | 2100 | 1454 | 10628 |
|  |  | 435 TOP2 | 1650 | 2100 | 10068 | 10629 |
|  |  | 435 ESP TOP2 | 1550/ 1650 | 2100 | 10069 | 10630 |
| Cummins 1993 – 1998 | N14 CPL 2026 | 370/435 ESP | 1450/ 1550 | 1800 | 1433 | 10510 |
|  |  | 410 | 1450 | 1800 | 1430 | 10509 |
| Cummins 1993 – 1998 | N14 CPL 2027 | 330 | 1350 | 1800 | 1415 | 10606 |
|  |  | 330/410 ESP | 1350/ 1450 | 1800 | 1427 | 10607 |
|  |  | 350 | 1350 | 1800 | 1417 | 10608 |
|  |  | 350 | 1350 | 2100 | 1418 | 10609 |
|  |  | 350 | 11400 | 1800 | 1420 | 10610 |
|  |  | 370 | 1400 | 1800 | 1422 | 10611 |
|  |  | 370 | 1450 | 1800 | 1425 | 10612 |
|  |  | 370 | 1450 | 2100 | 1426 | 10613 |
|  |  | 370 | 1450 | 2100 | 1561 | 10614 |
|  |  | 330 ESP TOP2 | 1350/ 1450 | 1800 | 10061 | 10615 |
| Cummins 1993 – 1998 | N14 CPL 2389 | 330 | 1350 | 1800 | 10149 | 10631 |
|  |  | 370 | 1450 | 1800 | 10156 | 10632 |
|  |  | 370 | 1450 | 2100 | 10157 | 10633 |
|  |  | 370 | 1450 | 2100 | 10342 | 10634 |
| Cummins 1993 – 1998 | N14 CPL 2390 | 370/435 ESP | 1450/ 1550 | 1800 | 10161 | 10635 |
|  |  | 370 ESP TOP2 | 1450/ 1550 | 1800 | 10242 | 10636 |
| Cummins 1993 – 1998 | N14 CPL 2391 | 435 | 1450 | 1800 | 10170 | 10637 |
|  |  | 435 | 1450 | 2100 | 10172 | 10638 |
|  |  | 435 | 1550 | 1800 | 10173 | 10639 |
|  |  | 435 | 1650 | 2100 | 10176 | 10640 |
|  |  | 435/500 ESP | 1550/ 1650 | 2100 | 10180 | 10641 |
|  |  | 460 ST2 | 1650/ 1850 | 1800 | 10261 | 10642 |
|  |  | 460 | 1650 | 2100 | 10184 | 10643 |
|  |  | 500 | 1650 | 2100 | 10186 | 10644 |
|  |  | 525 | 1850 | 2100 | 10191 | 10645 |
|  |  | 435 TOP2 | 1650 | 2100 | 10246 | 10646 |
|  |  | 435 ESP TOP2 | 1550/ 1650 | 2100 | 10248 | 10647 |
| Detroit Diesel Corp. 1994 – 19987 | S60 6067-GK60 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 19987 | S60 6067-GK28 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 1998 | S60 6067-TK60 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 1998 | S60 6067-TK28 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 1998 | S60 6067-PK60 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 1998 | S60 6067-PK28 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 19985 | S60 6067-WK60 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 19985 | S60 6067-WK28 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 19946 – 19987 | S60 6067-SK60 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 19946– 19987 | S60 6067-SK28 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 1998 | 6067-EK60 | ESN 6R157655 through 6R472018 |
| Detroit Diesel Corp. 1994 – 1998 | 6067-EK28 | ESN 6R157655 through 6R472018 |
| Mack 1994 – 1998 | EM7-275 | ESN 4B through 8R |
| Mack 1994 – 1998 | EM7-300 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-300 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-310/330 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-330/350 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-350 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-355/380 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-375 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-400 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-427 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-454 | ESN 4B through 8R |
| Mack 1994 – 1998 | E7-460 | ESN 4B through 8R |
| Renault VI 1993 –1998 | MIDR06.02.26M/2 | Engine Family Name (EFNa) PRE0377FAC9 |
| Renault VI 1993 –1998 | MIDR060226L511 | EFNa: SR3377D8DAAW, TR3377D8DAAW, and VR3377D8DAAW |
| Renault VI 1993 –1998 | MIDR060226M511 | EFNa: SR3377D8DABW, TR3377D8DABW, and VR3377D8DABW |
| Navistar/International 1998 | DT 466E | Engine Family Number (EFN) WNVXH0466FNA |
| Navistar/International 1998 | DT 466E | EFN: WNVXH0466CCB, WNVXH0466FNC |
| Navistar/International 1998 | DT 466E | EFN: WNVXH0466CCD |
| Navistar/International 1998 | 530E | EFN: WNVXH0530FNA, WNVXH0530CCB |
| Navistar/International 1998 | 530E | EFN: WNVXH0530FNC, WNVXH0530CCD |
| Volvo 1994 – 1998 | VE D12 | Engine Family Name (EFNa) RVT12.EJDBRA |
| Volvo 1994 – 1998 | VE D12 | EFNa: SVT12.EJDBRA, TVT12.EJDBRA |
| Volvo 1994 – 1998 | VE D12A | EFNa: VVT12.EJDBRA |
| Volvo 1994 – 1998 | VE D12B-345 EPG | EFNa: WVTXH12.150S |
| Volvo 1994 – 1998 | VE D12B-385 EPG | EFNa: WVTXH12.150S |
| Volvo 1994 – 1998 | VE D12B-425 EPG | EFNa: WVTXH12.150S |
| Volvo 1994 – 1998 | VE D12B-345 VEB | EFNa: WVTXH12.150S |
| Volvo 1994 – 1998 | VE D12B-385 VEB | EFNa: WVTXH12.150S |
| Volvo 1994 – 1998 | VE D12B-425 VEB | EFNa: WVTXH12.150S |
| Volvo 1994 – 1998 | VE D7C-275 | EFNa: WVTXH07.350S |
| Volvo 1994 – 1998 | VE D7C-300 | EFNa: WVTXH07.350S |

(6)	“Low NOx Engine Manufacturer” means an engine manufacturer that was required to develop Low NOx Rebuild Kits under (b)(4).

(67)	“MHDDE” means a heavy-duty diesel engine certified as a motor vehicle medium heavy-duty engine in accordance with title 13, California Code of Regulations, section 1956.8.

(78)	“Offset project” means a project conducted under applicable provisions in part IX.C of the Heavy Duty Diesel Engine Settlement Agreements with California and Consent Decrees with the United States Environmental Protection Agency.  The California Settlement Agreements and federal Consent Decrees are identified in title 13, California Code of Regulations, section 1956.8 (a)(2)(A), footnote 1.

(89)	“Owner” has the same meaning as title 13, California Code of Regulations, section 2180.1 (a)(21).

(910)	“Registered outside of California” means any of the following:

(A)	A heavy-duty diesel-powered vehicle operating in California under the terms of Interstate Reciprocity Agreements as authorized by Article 3 (commencing with section 8000), Chapter 4, Division 3 of the Vehicle Code and which belongs to a fleet that is not based in California;

(B)	A heavy-duty diesel-powered vehicle operating in California under the terms of any other apportioned registration, reciprocity, or bilateral prorate registration agreement between California and other jurisdictions and which belongs to a fleet that is not based in California; or

(C)	A heavy-duty diesel-powered vehicle operating in California under a short-term vehicle registration or permit of 90 days or less (including but not limited to 90-day temporary registrations and 4-day permits under Vehicle Code section 4004).

- Standards.

- On and after the applicable implementation date in subsection (d), and, except as provided in (e)(2), a vehicle propelled by a Low NOx Rebuild Engine must not operate on highways within the State of California without a Low NOx Rebuild Kit installed that meets the following emission requirements:

| Software Upgrade Requirements |
| --- |
| Option A (1994 – 1998) | Option B (1993 – 1998) |
|  | MHDDE | HHDDE |  | MHDDE | HHDDE |
| Euro III | 6.0 g/bhp-hr | 7.0 g/bhp-hr | Euro III | 6.5 g/bhp-hr | 7.5 g/bhp-hr |
| NTE | 7.5 g/bhp-hr | 8.75 g/bhp-hr | NTE | 8.1 g/bhp-hr | 9.38 g/bhp-hr |

| Manufacturer Option for Software Upgrade |
| --- |
| Company | Option | MY Year |
| Caterpillar | B | 1993 - 1998 |
| Cummins | B | 1993 - 1998 |
| Detroit Diesel Corporation | A | 1994 – 1998 |
| Mack | A | 1994 – 1998 |
| Navistar | not applicable | 1998 (only) |
| Volvo | A | 1994 – 1998 |
| Renault | B | 1993 - 1998 |

- A Low NOx Rebuild Engine manufacturer’s authorized dealers, distributors, repair facilities, and rebuild facilities, except as provided in (e)(2), must:

(A)	provide upon request and at no added cost a Low NOx Rebuild Kit to the owner or driver of a vehicle with a Low NOx Rebuild Engine, and to any non-affiliated rebuilder or other person; and

(B)	install the Low NOx Rebuild Kit within a reasonable amount of time.

(3)	Except as provided in (e)(2), Low NOx Rebuild Engine mManufacturers must reimburse authorized dealers, distributors, repair facilities, and rebuild facilities for their costs to install Low NOx Rebuild Kits on Low NOx Rebuild Engines, at the reimbursement cost level paid under the Consent Decrees and Settlement Agreements.  Low NOx Rebuild Engine mManufacturers may choose to reimburse at a rate above the reimbursement cost level paid under the Consent Decrees and Settlement Agreements.   incurred to meet the requirement in (2) to ensure that those identified in (2) pay no added cost.

(34)	No person may install on a Low NOx Rebuild Engine any engine software containing electronic control strategies, other than a Low NOx Rebuild Kit.

(45)	Any person installing a Low NOx Rebuild Kit must affix a label to each engine at time of installation.  The label must do all of the following:

- The label must contain an identifiable characteristic allowing the ARB to determine whether a Low NOx Rebuild Engine has had the appropriate Low NOx Rebuild Kit installed.  This identifiable characteristic may be a unique part number or other marking on the engine control module;

(B)	The label must contain a statement with appropriate blank spaces for the individual performing the installation to indicate when and by whom the Low NOx Rebuild Kit was installed on the engine;

(C)	The label must be placed in such a location as approved by the ARB consistent with California law;

(D)	The label must be fabricated of a material suitable for the location in which it is installed; and

(E)	The label must not be readily removable intact.

(56)	The owner of a vehicle cited for violating (c)(1) of this section must submit proof of Low NOx Rebuild Kit installation, as identified in title 13, CCR, section 2186, within 45 days of personal or certified receipt of the citation.

(7)	Any Low NOx Rebuild Manufacturers’ authorized dealers, distributors, repair facilities, or rebuild facilities, except as provided in (e)(2), refusing to install a Low NOx Rebuild Kit upon request, or failing to install a Low NOx Rebuild Kit within a reasonable amount of time from that request, shall be subject to a civil penalty of $500 per incident.

- Implementation Dates.

- 1993 and 1994 model year Low NOx Rebuild Engines, except as provided in (e)(2), must have a Low NOx Rebuild Kit installed by April 30, 2005.

- 1995 and 1996 model year Low NOx Rebuild Engines, except as provided in (e)(2), must have a Low NOx Rebuild Kit installed by August 31, 2005.

- 1997 and 1998 model year Low NOx Rebuild Engines other than MHDDE, except as provided in (e)(2), must have a Low NOx Rebuild Kit installed by December 31, 2005.

(4)	1997 and 1998 model year MHDDE Low NOx Rebuild Engines, except as provided in (e)(2), must have a Low NOx Rebuild Kit installed by December 31, 2006.

(e)	Exemptions.

(1)	A Low NOx Rebuild Engine receiving a software upgrade performed as part of an approved incentive or offset project prior to the adoption of Section 2011 is exempt from the requirements in (c).

(2)	Low NOx Rebuild Engines identified in (b)(5) as a make and year of Detroit Diesel Corp. (DDC) are exempt from the requirements of this regulation, as the Board has found that DDC has met the first voluntary program target and is on track to meet future targets under the voluntary program.  Owners, authorized dealers, and distributors of these engines, and repair and rebuild facilities for these engines, are likewise exempt from the provisions of this regulation with respect to these engines.in (c), provided that DDC voluntarily installs Low NOx Rebuild Kits at the following rate:

(A)	Low NOx Rebuild Kits must be installed on 60 percent of DDC’s Low NOx Rebuild Engines no later than May 31, 2005;

(B)	Low NOx Rebuild Kits must be installed on 80 percent of DDC’s Low NOx Rebuild Engines no later than January 31, 2006; and

(C)	Low NOx Rebuild Kits must be installed on 100 percent of DDC’s Low NOx Rebuild Engines no later than January 1, 2008.

(3)	A Low NOx Rebuild Engine manufacturer subject to the provisions in (e)(2) shall report the number of Low NOx Rebuild Kit installations with the dealership name and address, the date of installation, vehicle identification number, engine make and model year, and ESN for each installation.  Reports shall be submitted electronically to the Executive Officer or designated representative on the following schedule:

(A)	Submit a report on June  7, 2005, of Low NOx Rebuild Kits installed from October 28, 2004, through May 31, 2005.

(B)	Submit a report on February 7, 2006, of Low NOx Rebuild Kits installed from June 1, 2005, through January 31, 2006.

(C)	Submit a report on January 7, 2008, of Low NOx Rebuild Kits installed from February 1, 2006, through December 31, 2007.

(4)	The Executive Officer shall review each report in (3), applying the criteria in Appendix A, to determine if a Low NOx Rebuild Engine manufacturer has met the next installation rate in (e)(2), if any, and to consider whether the manufacturer’s installation progress is sustainable toward meeting the next installation rate in (e)(2), if any.

- If the Executive Officer determines that a Low NOx Rebuild Engine manufacturer has not met the installation rate in (e)(2), an Executive Officer public hearing shall be convened to consider removing the exemption for that manufacturer’s engines.

- If the Executive Officer hearing results in the Low NOx Rebuild Engine manufacturer’s engines being subject to the requirements in (c) within the date range below, the compliance schedule requiring installation of Low NOx Rebuild Kits on the manufacturer’s 1994 through 1998 model year Low NOx Rebuild Engines is as listed here:

Date Range	Compliance Schedule

April 30, 2005 – September 30, 2005	December 31, 2005

October 1, 2005 – September 30, 2006	December 31, 2006

October 1, 2006 – July 1, 2007	December 31, 2007

- Any determination under (A) that results in subjecting a manufacturer’s engines to a compliance schedule in (B) will be communicated to affected persons and published in the California Regulatory Notice Register.

(f)	Severability.

If any provision of this section or the application thereof to any person or circumstances is held invalid, such invalidity shall not affect other provisions or applications of the section that can be given effect without the invalid provision or application, and to this end the provisions of this section are severable.

(g)	The requirements in (c)(2) and (c)(3) are a declaration of existing legal obligations.

NOTE: Authority Cited: Sections 39600, 39601, 43013, 43018, and 43701, Health and Safety Code.  Reference: Sections 39001, 39003, 43000, 43013, 43016, and 43018, Health and Safety Code.

Appendix A

Voluntary Software Upgrade Program Discussion Paper (March 16, 2004)