Appendix E

Stationary Diesel-Fueled Engines

Health Risk Assessment Methodology

# Introduction

This appendix presents the methodology used to estimate the potential cancer risk from exposure to diesel particulate matter (PM) emitted from diesel-fuel stationary engines.  The methodology was developed to assist in development of the Stationary Diesel-Fueled Engine Airborne Toxic Control Measure (ATCM).

The estimated risks and assumptions used to determine these risks are not based on a specific engine location or operating parameters.  Instead, general assumptions bracketing a fairly broad range of possible operating scenarios were used.

Exposures were estimated at varying downwind distances, including the “point of maximum impact” (PMI) as determined using air dispersion modeling.  The estimated risk ranges are used to provide a “qualitative” assessment of the potential risk levels near operating stationary diesel-fueled engines.  Actual risk levels will vary due to site specific parameters, including horsepower rating and configuration of the engine, emission rates, operating schedules, site configuration, site meteorology, and distance to receptors.

# Source Description

The following methodology was developed to provide estimates of the potential cancer risk associated with exposures to diesel PM emissions from stationary diesel-fueled engines.

Stationary diesel-fueled engines are generally categorized as either prime engines or emergency back-up engines.  Prime engines are used to power equipment such as compressors, cranes, generators, pumps, and grinders.  Emergency back-up engines are used solely for emergency back-up electric power generation or water pumping.  The main difference between prime and emergency back-up engines is that prime engines usually operate considerably more hours per year.

The methodology used in this risk assessment is consistent with the Tier-1 analysis presented in the draft Office of Environmental Health Hazard Assessment (OEHHA), Air Toxics Hot Spots Program Risk Assessment Guidelines: The Air Toxics Hot Spots Program Guidance Manual for Preparation of Health Risk Assessments (OEHHA, 2002a).  The OEHHA draft guidelines and this assessment utilize health and exposure assessment information that is contained in the Air Toxics Hot Spot Program Risk Assessment Guidelines, Part II, Technical Support Document for Describing Available Cancer Potency Factors (OEHHA 2002b); and the Air Toxics Hot Spot Program Risk Assessment Guidelines, Part IV, Technical Support Document for Exposure Analysis and Stochastic Analysis (OEHHA 2000), respectively.

# Modeling Assumptions

For this modeling exercise we used a matrix of parameters.  We modeled engines of 200, 550, and 1500 horsepower, and varied both the emissions rate and the hours of operation for each horsepower rating.  For each engine horsepower, we modeled five diesel PM emission factors: 0.01, 0.15, 0.40, 0.55, and 1.0 grams/brake hp-hour.  We also varied the hours of operation and evaluated the risks for the following hours of operation: 10, 20, 30, 40, 50, 100, 200, 300, 400, 500, and 1000 hours/year.  For each case we calculated the risk at varying downwind distances.

# Model Used

The PM emissions are modeled in this scenario using the United States Environmental Protection Agency’s Industrial Source Complex Short Term Model – Version 3 (ISCST3 Date: 00101).  The ISCST3 is an air dispersion model that allows an estimation of the annual average above ambient diesel PM concentrations.  The potential cancer risk to nearby residential receptors is obtained by multiplying annual average above ambient concentration of diesel PM by the unit risk factor (URF) for diesel PM (300 excess cancers/ug/m3 over a 70-year exposure period).  The results are expressed as an estimate of potential cancer risk in chances per million.

Meteorological Data

Meteorological data are site-specific parameters that are used in air dispersion models to calculate concentrations of emissions and subsequent risk.  For this scenario, West Los Angeles, 1981, meteorological data were selected as the input to the ISCST3 model.  The West Los Angeles meteorological data tend to provide higher estimates of risk than most of the other meteorological data sets compiled by ARB.  This is because the West Los Angeles site tends to have the lowest average wind speed and more persistent wind directions, which result in less dispersion of pollutants.

# Model Parameters and Emission Factors

The key modeling parameters and emission factors are presented in Table 1.  We used the rural dispersion coefficient to provide a more conservative (higher) estimate of the predicted concentration and the estimated potential cancer risk.

# Table 1:  Modeling and Health Risk Assessment Parameters

| Modeling Paramenters |  |
| --- | --- |
| Model | ISCST3 (Version 00101) |
| Engine Horsepower (at 100% load) | 200 HP, 550 HP, 1500 HP |
| Engine Operation Load | 75% |
| Emission Factor | 0.01, 0.15, 0.40, 0.55, 1.00 g/bhp-hr |
| Operation Hours (annual) | 10, 20, 30, 40, 50, 100, 200, 300, 400, 500, 1000 |
| Source Type | Point |
| Dispersion Setting | Rural |
| Receptor Height | 1.5 m |
| Stack Information: |  |
| Stack Diameter | 4 in, 6 in, and 13 in |
| Stack Height | 3 m |
| Stack Temperature | 622 K |
| Stack Exhaust Velocity | 59.8 m/s, 73.1 m/s, and 42.5 m/s |
| Time Emissions Emitted | 3 p.m. |
| Meteorological Data | West L. A. (1981) |
| Release Height | Same as the stack height |
| Health Risk Assessment Parameters |  |
| Receptor’s Hypothetical Exposure Time | 70 years, 50 weeks per year |
| Adult Daily Breathing Rate Range | 271 - 393 l/kg body weight -day 1 |
| Adult Body Weight | 70 kg |
| Diesel PM Unit Risk Factor | 300 excess cancers/(g/m3 |

### 1.  The low end of the breathing rate range is the mean of the OEHHA breathing rate distribution and the high end is the 95th percentile of the distribution

### Results

We have included three sets of tables, one set for each modeled horsepower (200, 500, and 1500).  Each set of tables contains five sub-tables, one for each emission factor (0.01, 0.15, 0.40, 0.55 and 1.0 g/bhp-hr).  Each emission factor table comprises a matrix of downwind distances and hours of operation, with the calculated risks for each combination.  The low-end and high-end of the risks presented in the tables are corresponding to the 65th (mean) and 95th percentile breathing rates, respectively.  Additionally, the tables are coded using varied levels of shading.  The moderately shaded squares denote the low-end potential cancer risks of between one and ten per one million people.  The darkest squares show the low-end risk levels between 11 and 100 potential cancer cases per million.  The white squares show the highest calculated risks, those exceeding 100 potential cases per million people.  As can be seen, the estimated cancer risk from stationary diesel-fueled engines varies depending on the emission rate, horsepower and annual hours of operation for a given engine.

Estimated risk as a function of emission factor:

For the range of engine horsepowers modeled, all those engines that emitted

0.01 g/bhp-hr or less could run at least 1000 hours per year without exceeding the lowest range of estimated risks, those of 10 or less potential cancer cases per year.

For the 0.15 g/ bhp-hr engines, most combinations of horsepower, hours of operation and downwind distance did not exceed the lowest range of risks, with those combinations resulting in the higher risk ranges occurring at 200-plus operating hours and low to moderate downwind distances.

For engines with emissions of 0.4 g/bhp-hr or more the trend was to find higher risks at low to moderate downwind distances and longer operating times continues, with the proportion of moderate to high risk level results increasing as emission factors increase.

Estimated risk as a function of hours of operation:

Generally, as the hours of operation increased, the number of engines that exceeded the lowest risk range increased.  However, most engines could operate for 10 to 20 hours per year without exceeding the lowest range of risk.

Estimated risk as a function of horsepower:

For the engine configurations evaluated in these scenarios, the smaller horsepower engine (200 hp), typically demonstrated higher near source risk for a given number of hours of operation than the larger engines.  In addition, the potential cancer risk reached the point of maximum impact more rapidly for the 200 hp engine than the larger engines.  The larger engines had the point of maximum impact further from the engine due to the greater plume dispersion that occurs with the large horsepower engines.

REFERENCES:

Office of Environmental Health Hazard Assessment.  Air Toxics Hot Spots Program Risk Assessment Guidelines:  The Air Toxics Hot Spots Program Guidance Manual for Preparation of Health Risk Assessments; 2002.  (OEHHA, 2002a)

Office of Environmental Health Hazard Assessment.  Air Toxics Hot Spots Program Risk Assessment Guidelines, Part II, Technical Support Document for Describing Available Cancer Potency Factors; 2002.  (OEHHA, 2002b)

Office of Environmental Health Hazard Assessment.  Air Toxics Hot Spots Program Risk Assessment Guidelines, Part IV, Technical Support Document for Exposure Analysis and Stochastic Analysis; 2000.  (OEHHA, 2000)

# Footnotes

1The pollutant concentrations obtained from this modeling exercise that are used to estimate cancer risk do not include the background (or ambient) levels of the modeled pollutant.  The final risk value is determined by multiplying the modeled pollutant concentration by the Unit Risk Factor (URF), as determined by ARB and the Office of Environmental Health Hazard Assessment (OEHHA).